## Slide 1: The Confederation of Finnish Construction Industries: Product information and supply chain digitalization development project
Engineer-To-Order products
2025-03-07 / Presentation
BETK-workgroup
Notes: BETK kalvostoBETK kalvosto

## Slide 2: Contents
Motivation
Background
  Manufacturing strategies
  T-Model
  Preliminary study on the current state of the ETO Supply Chain
Project Organization
Work Objective
  Road-map
  Future State Data Flow Architecture for an ETO products
Work Tasks
  Standardization work group
  API & IT infrastructure

## Slide 3: Identified Challenges in Information Flow in the Construction Industry
Closed Information Exchange Solutions Between Stakeholders Point-to-point solutions operating in a closed environment are inefficient and costly, as each system pair requires a separate solution
FM
Contractor
Supplier
Design
Engineer
Silo thinking fragments workflows, weakens communication, and reduces efficiency when stakeholders define matters separately without collaboration.
Developer
The lack of machine-readable structured information prevents the automation of processes in the construction industry.
1. kerros
1. krs
1
?
Manual Processing of Unstructured Information
(e.g., PDF, PNG, email, phone calls)
Requires human interpretation and inefficient manual work, increasing the risk of errors as the same information is repeatedly generated, stored, lost, and archived.
.PDF
.PDF
.PDF
Lack of standardization and interoperability in information management processes prevents industry development.
?
Notes: RT:n tuotetiedon ja toimitusketjun digitaalisen hallinnan kehityshankkeessa kartoitettuja ja esiin tulleita haasteita rakennusalan tiedon virtauksen näkökulmasta
Rakennusalalla on ollut vuosikausia avoimuuteen ja yhteentoimivuuteen liittyviä haasteita. Rakennusalalla eri osapuolet työskentelevät usein siiloissa määrittelemällä kohteita, ominaisuuksia ja käyttötarkoituksia ilman, keskinäistä yhteistyötä. Tämä hajanainen lähestymistapa on estänyt alaa saavuttamasta yhtenäistä digitaalista kehitystä.

## Slide 4: Digitization
Are we aiming for digitization or digitalization?
Digitalisation
Converting information into a digital "image" of the data.
  Converting native software files (Word, Excel, etc.) into digital "images," such as PDFs
  Converting native BIM into IFC without machine-readable standardization of data content.
The data is not machine-readable and requires human intervention
Transforming data into a structured format so that it can be transferred automatically and seamlessly between systems
Requires the definition of metadata.
The goal is to create new ways to use, analyze, and manage data more efficiently

## Slide 5: Why should we strive for digital supply chain management?
€
CO2-emissions
Work safety
Time
Quality
Notes: The well known industry challenges are:
In addition, recent research work and our national situation tells a story that something needs to change.
So, why should we strive for digital supply chain management?
To ensure better quality,
To spend our valuable time to more productive work,
Improve work safety,
Automate the manage of CO2 emission estimations
And the most important factor is to save money

## Slide 6: Contents
Motivation
Background
  Manufacturing strategies
  T-Model
  Preliminary study on the current state of the ETO Supply Chain
Project Organization
Work Objective
  Road-map
  Future State Data Flow Architecture for an ETO products
Work Tasks
  Standardization work group
  API & IT infrastructure

## Slide 7
PROJECT-SPECIFIC PRODUCTS
OFF-THE-SELF PRODUCTS
Engineer-To-Order
Make-To-Order
Assemble-To-Order
Make-To-Stock
PRODUCTION STRATEGIES FOR BUILDING PRODUCTS

## Slide 8
U
Order Penetration Point (OPP), where push control transitions to pull control.
Product design
Parts manufacturing
Assembly
Storage
source: https://www.logistiikanmaailma.fi/tuotanto/tilauksen-kohdennuspiste-opp/
Make-To-Stock
Assemble-To-Order
Eg. Ready mix concrete
Make-To-Order
Eg. Doors, windows
Engineer-To-Order
Eg. Precast concrete
PRODUCTION STRATEGIES
Delivery
Different production strategies for building products delivered to the site
A challenge for the procurement process, production planning, and design that has neither been identified nor solved from the perspective of information management.
OPP
OPP
OPP
OPP

## Slide 9: Preliminary study on the current state of the ETO Supply Chain
The BETK project was initiated through supply chain workshops consisting of experts, aiming to map the current process of the precast concrete element (sandwich + partition wall) supply chain, covering all stages from design to installation, and to identify issues occurring in different parts of the supply chain.
In these workshops, each stage of the process was analyzed, including the involved stakeholders, current information exchange methods and formats, as well as encountered challenges.
The key findings were related to information flow between different phases of the supply chain.
Reference: Alaluusua, T. (2023) Digital management of information exchange in takt production supply chains
Notes: BETK-projekti lähti käyntiin toimitusketjutyöpajojen kautta, jossa tavoitteena oli kartoittaa betonielementin (seinä) toimitusketjun nykyprosessia kattaen toimitusketjun vaiheet suunnittelusta asennusvaiheeseen, ja koota yhteen toimitusketjun eri osissa ilmeneviä ongelmia.
Työpaja koostui kolmesta työvaiheesta. Ensimmäisessä vaiheessa toimitusketjun prosessikaaviolle asetettiin aikajärjestykseen toimitusketjun prosessivaiheet. Toisessa vaiheessa prosessikaavioon lisättiin toimitusketjun eri vaiheissa tarvittavat tietosisällöt ja välitettävät tiedot/sanomat. Lopuksi prosessikaavioon lisättiin toimitusketjun eri vaiheissa yleisesti esiintyviä ongelmia.
Työpajan tulokset käytiin läpi Juurisyyanalyysissa, jossa ongelmat perattiin keskustelujen kautta selvittäen ongelmien juurisyyt, -seuraukset ja näiden luokittelut.

## Slide 10: Towards (true) Supply Chain Management
T-Model describes the value chain of the project to be built (→) and the supply chain of the product to be linked to it (↑)
WP
13
WP
14
WP
15
WP
16
WP
17
WP
18
PLANNING & DESIGN
CONSTRUCTION
SUPPLY CHAINS
PROCUREMENT
erp
Product Delivery
Assembly
Parts manufacturing
Product Design
Architectural Design
Structural Design
MEP
Design
Cost
Estimation
.ifc
Project Development
WP
1
WP
2
WP
3
WP
4
WP
5
WP
6
WP
7
WP
8
WP
9
WP
10
WP
11
WP
12
Make-To-Stock, MTS
Assemble-To-Order, ATO
Make-To-Order, MTO
Engineer-To-Order, ETO
OPP
OPP
OPP
OPP
OPP = Order Penetration Point
Notes: Here is presented T-Model that….
The supply chains can be classified based on different production models (MTS, ATO, MTO, ETO).
The Order Penetration Point (OPP) determines where product supply chain shifts from a push (forecast-driven) to a pull (order-driven) system.
Precast concrete supply chains follow Engineer-To-Order (ETO) logic, requiring extensive collaboration between structural designers, contractors, manufacturers, transporters, and installers.
These multi-party networks face challenges in integrating design, production, and installation processes, with significant information exchange needed before the product exists.

## Slide 11: CAUSE MAP BASED ON WORKSHOP RCA
ERECTION
DELIVERY
MANUFACTURING
PROCUREMENT
Installation problem
Gaps in source data
Incomplete/incorrect plans
Plan change information exchange challenges
DESIGN
Production schedule too tight
(Element factory unable to deliver elements)
Faulty/damaged element
Technical problems
Long-term storage on site
Lack of reception inspection
Lack of a snapshot of the installation phase
Inadequate reception inspection
Incorrect concrete element delivered/on the wrong site
Element not found/identified on site
Delays caused by a slow procurement process
(Human errors during the procurement/tender phase)
Human error in production
Production delays
Failure to produce due to poor planning
Human error in design
Slow design process
Difficulties in exchanging information about changing timetables
Production schedule changes
Order changes
Errors relating to the quantity or quality of the products offered
Difficulties in unloading
Communication problems in managing products & deliveries
Post-contract plan changes / procurement errors due to plan deficiencies
Problems with information exchange
(lack of snapshot of the delivery & different ways of working)
Delivery problems (loading order, delivery content)
Delivery does not arrive as agreed (punctuality in terms of time or content)
Notes: Based on these findings, we organised several supply chain process workshops with different construction industry stakeholders involved in this supply chain to understand how the precast concrete supply chain works. These workshops identified each process step, and the parties involved, the current information exchange methods and formats used, and the problems encountered.
The key findings were related to information flow between different supply chain stages.

## Slide 12: Preliminary Study on the Current State
Chart: Disruption of errors in the frame erection phase
| Design | Precasting | Element transportation to the site | Other deliveries | Site logistics | Measurements | Crane and lifting | On-site installation
Severe | 4 | 9 | 10 | 5 | 0 | 0 | 5 | 2
Harmful | 9 | 11 | 13 | 3 | 5 | 1 | 0 | 4
Minor | 8 | 22 | 15 | 0 | 5 | 2 | 2 | 12
Measurements on four different sites
Measurement period: 50 total workdays
Minor Disruption
Work becomes slightly more challenging or slows down a bit. Disruption duration is often less than 30 minutes.
Harmful Disruption
Work slows down significantly or requires expensive measures. Disruption duration over 30 minutes.
Severe Disruption
Work becomes slightly more challenging or slows down a bit. Disruption duration is often less than 30 minutes
Reference: Makkonen, S. (2023) Improving process flow in frame erection phase of a residential building

## Slide 13
Rakentamisen toimitusketjuissa piilevät ongelmat
(suljettu toimintaympäristö)
Point-to-point ratkaisut
(keskitetty tiedonvaihto)
Rakenteeton tiedonvaihto (pdf, kuvat, puhelut, sähköpostit)
Vakioimaton tietosisältö (itse määritetyt arvot)
v
v
v
SUUNNITTELU
VALMISTUS
TOIMITUS
YLLÄPITO
Projektipankki
IFC
IFC
Projektipankki
HANKINTA
ASENNUS
IFC
DWG
INFORMAATIO EI VIRTAA!
INFORMAATION VÄLITYS ON MANUAALISTA!
INFORMAATIO ON RAKENTEETONTA!
INFORMAATIO EI OLE KONELUETTAVAA!
PDF
PDF
PDF
PDF
DWG
© Teemu Alaluusua
Notes: ”Rakennusalalla valtaosa nykyisin välitettävästä tiedosta ei ole koneluettavaa, koneymmärrettävää eikä automaattisesti käsiteltävää. Rakenteettoman ja vakioimattoman tiedonvaihdon seurauksena, ihminen on joka välissä tuottamassa, tallentamassa, hukkaamassa ja arkistoimassa samaa tietoa moneen kertaan.
Toimitusketjujen nykyinen tietoarkkitehtuuri
(suljettu toimintaympäristö)
Tiedonvaihdossa hyödynnetään point-to-point-ratkaisuja, jotka ovat tehottomia ja kalliita, koska jokainen järjestelmäpari tarvitsee oman ratkaisun
Yhteentoimivuuden (standardien) puute ei mahdollista toimialan kehitystä
Strukturoimaton data (pdf, kuvat, puhelut, sähköpostit) tiedonvaihdossa.

## Slide 14: Example problems
MALLIPUU
(B) LVI KOHDE X
(B) Tontti.1
(B) mc-building
(B) Ryomintatila
(B) 1. kerros
(B) 2. kerros
(B) 3. kerros
(C) RAK KOHDE X
(C) KOHDE X
(C) Rakennus.r.1
(C) 0
(C) 1
(C) 2
(C) Kerros. 3
The same building, but different designers use different naming conventions for identifying floors.
[number]. Floor
[number]
Floor. [number]
A human can resolve this by reasoning, but a machine cannot. Automated data transfer is not possible with such information.
Information management using manual methods in practice:People do their best with the available methods and tools.
INSTALLING
DESIGN
Notes: Esimerkkinä suunnitteluvaiheen digitaalisen tiedon tuottamisen ongelma (vakioimattomat tietosisällöt)
Esimerkkinä asennusvaiheen manuaaliset tuotannonhallinta menetelmät ja digitalisaation puute.

## Slide 15: Contents
Motivation
Background
  Manufacturing strategies
  T-Model
  Preliminary study on the current state of the ETO Supply Chain
Project Organization
Work Objective
  Road-map
  Future State Data Flow Architecture for an ETO products
Work Tasks
  Standardization work group
  API & IT infrastructure

## Slide 16
Project organisation
The Confederation of Finnish Construction Industries (RT) is currently running a development project focused on digitalizing product information and supply chain management in construction. A steering group guides the development, and its members vary according to the supply chain groups.
The development work is carried out in supply chain work groups, which are divided according to the production methods (MTS, ATO, MTO, ETO).
The working groups are composed of construction companies, associations, supply chain experts, academics and public sector actors. The project aims at an integrated and digital information management to improve the efficiency and transparency of supply chains.
STEERING GROUP
Information Assurance and Technology Group
SC group: BETK
”Precast concrete supply chain”
(Engineer-To-Order, ETO)
SC group:
(Assemble-To-Order, ATO)
SC group:
MEP-products
(Make-To-Stock, MTS)
THE ASSOCIATION PARTNERS
Aalto University
Building 2030
TATE 2030
GS1 Finland
SC group :
(Make-To-Order, MTO)
INDUSTRY STAKEHOLDERS
SKOL ry (the association of consulting firms)
RAKLI ry (association of professional property owners, real estate investors, corporate real estate managers and construction clients in finland)
National product databases
COMPANIES
Confederation of Finnish Construction Industries (RT) Product Information and Supply Chain Digitalisation Development project (2024  Future)
GOVERMENT
Ympäristöministeriö
Ministry of the Environment
Valtiokonttori
Finnish Peppol Authority
Verohallinto
Tax administration
Supply chain workgroups

## Slide 17: SC group: BETK
Actors involved
BETK is part of the Confederation of Finnish Construction Industries RT’s development project for the digitalization of product information and the supply chain. Its goal is to digitalize the supply chain of engineer-to-order building products.
The BETK working group is divided into two subgroups, focusing on data standardization and data transfer interfaces.
Standardization work group
Antti Pekkala
Interface work group
Tom Partanen
SC group: BETK
Janne Kihula
Teemu Alaluusua

## Slide 18: Contents
Motivation
Background
  Manufacturing strategies
  T-Model
  Preliminary study on the current state of the ETO Supply Chain
Project Organization
Work Objective
  Road-map
  Future State Data Flow Architecture for an ETO products
Work Tasks
  Standardization work group
  API & IT infrastructure

## Slide 19: Product Information and Supply Chain Digitalisation Development project BETK-Supply Chain group
Transmission of transaction data (creation of electronic order-delivery messages for the construction industry) between supply chain stakeholders
(Peppol / UBL).
OBJECTIVE
Enabling interoperable and digitally managed data transfer in the supply chains of order-based designed building products:
Exchange of machine-readable information
Standardized data content
Uniform methods for information identification, recognition, and sharing processes
Availability of product data and recording of process data in the supply chai
Standardization of information content produced during the design phase and enriched in the supply chain to enable machine readability and automation.
Transmission of product information between supply chain stakeholders (National product databases + EU Digital Product Passport)
Purchase
Sale
Peppol network
Operator
Operator
Tender 
Order response 
Delivery confirmation 
Invoice 
Call for tender
Order
Call off
Notification
Invoice response
DPP
Standardization of the identification and recognition of supply chain components, locations, and stakeholders
(Application of GS1 standards)
sGTIN, SSCC, GLN jne.
Enabling interoperable sharing of transport and event data
WHO
WHAT WHERE WHEN WHY
Standardisation of process data sharing
Design
Manufactured
Transportation
Installing
TASKS
PARTICIPANTS
Construction industry companies
Data transfer expert companies
Academia
Public sector representatieves
Non-profit organizations

## Slide 20: Work Tasks
BETK develops and standardises solutions to support the flow of information and develops application guidelines for the construction sector.
The task of the working group is to promote the interoperability of information flows in accordance with the production strategy for custom-designed construction products and to promote the development of the industry through standardisation.
The BETK working group is divided into two working groups on information standardisation and interfaces for information transfer.
Transmission of transaction data (creation of electronic order-delivery messages for the construction industry) between supply chain stakeholders
(Peppol / UBL).
Standardization of information content produced during the design phase and enriched in the supply chain to enable machine readability and automation.
Transmission of product information between supply chain stakeholders (National product databases + EU Digital Product Passport)
Purchase
Sale
Peppol network
Operator
Operator
Tender 
Order response 
Delivery confirmation 
Invoice 
Call for tender
Order
Call off
Notification
Invoice response
DPP
Standardization of the identification and recognition of supply chain components, locations, and stakeholders
(Application of GS1 standards)
sGTIN, SSCC, GLN jne.
Enabling interoperable sharing of transport and event data
WHO
WHAT WHERE WHEN WHY
Standardisation of process data sharing
Design
Manufactured
Transportation
Installing
TASKS

## Slide 21: Key factors to enable digital supply chain management interoperability
Capture
Master data
Event data
Transactional data
1D & 2D Barcodes
RFID -tags
Share
Identify
Manufacturer
Item
Case
Pallet
Transport
Distributor
Transport
Case
Item
Store
Customer
GLN
GTIN
sGTIN
SSCC
GTIN
sGTIN
GRAI
SSCC
GTIN
sGTIN
GIAI
GLN
GIAI
SSCC
GTIN
sGTIN
GTIN
sGTIN
GLN
GSRN
GLN Global Location Number
GTIN Global Trade item Number
sGTIN Serialized Global Trade item Number
SSCC Serial Shipping Container Code
GRAI Global Returnable Asset Identifier
GIAI Global Individual Asset Identifier
GSRN Global Service Relation Number
Process data
status
Transport information
DPP
Product data
Quick Response (QR) codes
Digital Twin
GUID
Peppol
network
eFTI
CBV Core Business Vocabulary
GS1 EPCIS
(Electronic Product Code Information Services)
Notes: Digital supply chain management consist of information identification, data capture, and information sharing.
For information identification point of view, it is important to use globally used identification keys to identify physical and digital objects, documents, physical locations etc.
Data Capture (AIDC) refers to the methods of automatically identifying objects, collecting data about them, and entering that data directly into computer systems (i.e., without human involvement).”
Open information sharing solutions help the parties involved in supply chains to share and receive information efficiently and securely about products, deliveries and locations, and more.

## Slide 22
Roadmap for the digitalisation of construction supply chains
(ETO-products)
Digitalisation 1.0:
Digitising current construction processes
Digitalisation 2.0:
Digitalisation of responsible construction and the use of modern technology
Order-delivery process
Product data process:
GS1 standards
Design process:
Data dictionaries, reference data
Strategic objective
Digitalised way of working in construction
The procurement process: Company's own ERP/data platform
Implementing circular economy processes
Automated GWP and sustainability reporting
As-built data collection and digital delivery
Automatic calculation of the actual carbon footprint
E-supply chain management
Monitoring the carbon footprint of building design
Adoption of AI-based processes
Digital takt-production management
UPID
Product Identification
sGTIN
AIDC
Data Carriers
(2D codes / RFID)
Product data sharing
(ETIM, TT-standard)
EU DPP
(2027)
Reference data for for design
(data dictionaries)
Message based order-delivery process
(PEPPOL / EPCIS / eFTI)
(BIM) export to structural form
(E-BOM  M-BOM)
Design and product information digitally into procurement systems (ERP)
Notes: This figure shows a roadmap for the digitalisation of the construction supply chain, in particular for ETO (Engineer-To-Order) products.
The roadmap is divided into two main phases, Digitalisation 1.0 and Digitalisation 2.0, which symbolise the different stages of development in the digitalisation of the construction sector.
Digitalisation 1.0, lays the foundations for more advanced digital solutions and circular economy processes.
The Roadmap addresses the themes that are key to the digitalisation and standardisation of the ETO supply chain.
The ongoing development project have found solutions for Product identification and data carriers, and working on design process standardization and order-delivery process standardization related to transactional data sharing through Peppol messages, event data sharing by using GS1 EPCIS standard, and delivery data sharing by using eFTI.

## Slide 23: Standards that make systemic change possible
LOIN
Level Of Information Need
EN ISO
17412-1
EN ISO
7817-1
Peppol / UBL
EN ISO/IEC
19845:2015
BEAst slutrapport
ID: 14017
BEAst slutrapport
ID: 13915
Information management
Processes – how to work in the project using BIM
EN ISO
19650-1:2018
EN ISO
19650-2:2018
EN ISO
19650-3:2020
EN ISO
19650-4:2022
EN ISO
19650-5:2020
CEN/TR
17439
IFC
Data model –schema and format
EN ISO
16739:2024
Data templates, properties
EN ISO
22057:2022
EN ISO
23387:2020
EN ISO
23386:2020
IFD classification, SML
Data dictionaries, classification, linked data
EN ISO
12006-2:2020
EN ISO
12006-3:2022
https://bis.beast.se/
www.valtiokonttori.fi
https://docs.peppol.eu/
eFTI (EU)
CELEX
32020R1056
https://eur-lex. Europa.eu /eli/reg/2020/1056/oj
EPCIS (GS1)
GS1 EPCIS Standard:2022
www.epcis-sandbox.gs1.org
GS1 CBV Standard:2022
GS1 EPCIS & CBV Guideline:2023
Construction industry implementation guidelines
UPID + AIDC
BETK Implementation Guideline
GS1 Norway Guideline SGTIN and RFID:2018
https://GS1.org
EU DPP
XXXX XXXXX
-
EN ISO/IEC
16931-1:2017
GS1 Standards
Identification
GS1 GLN
ISO/IEC 6524
GS1 SSCC
ISO/IEC 15459-1 ISO/IEC 6523
GS1 GIAI
ISO/IEC 15459-4 & 5 ISO/IEC 6523
GS1 GSRN
ISO/IEC 15418
GS1 GRAI
GS1 GDTI
GS1 GTIN
ISO/IEC 15459-6
ISO/IEC 6523
GS1 Standards
Data Capture
GS1 Data Matrix
ISO/IEC 16022
GS1 QR Code
ISO/IEC 18004
EPC Tag Data Standard
ISO/IEC 15962:2024
EAN/UPC barcode
ISO/IEC 15420
GUID / UUID
ISO/IEC
9834-8:2005
ISO/IEC
11578:1996
Notes: From interoperability point of view, it is important to be aware of existing de facto standards, implementation guidelines, legislation for design process, product data process, supply chain management, information sharing. Here is listed a some of those existing ones that we are considering at our development work.

## Slide 24
DPP
Financial system
Project development
Distributed
architecture using message based system
Sale
Delivery
ID: SGTIN/SSCC
Data carrier: 128 bardcode/DataMatrix/RFID
Private Sector Information Services
Public sector
Information Services
(EU and National)
MANUFACTURING
PROCUREMENT AND SCM
PART MANUFACTURERS & SUPPLIERS
DESIGN
Architectural design
CONSTRUCTION
PRH: CSRD
EFRAG:XBRL: financial statement and sustainability report
Cost modelling
Structural design
MEP
design
ARC-BIM
Installation of element
Call-offs from site
Production planning
Initial delivery order
Receiving & storage
Element repairs
Digital Reception Inspection Installation and status information Digital process twin (log data)
Acceptance inspection
Final settlement of accounts
Order
Order confirmation
Factory fine scheduling
Rough capacity planning
Delivery-time confirmation
Delivery Notification
M-BOM
for each element
Warranty
Delivery confirmation
Common defects of element types
Space information
Elements spatial information
Transport CO2 data
Tender response
CO2 and sustainability reporting data
As Scheduled & As Manufactured
Invoice
Environmental balance sheet value accounting
CO2 and data for CEI
(Circular Economy Indicators)
Quantity
take-off
Data repositories, interfaces and key process functions for a digitised supply chain
Design Change Management
Building Control
Future state Data Flow Architecture for an ETO construction product from design to finished building
Product Information Database
As Scheduled
& As Performed
As Designed & As Build
Query-based data transfer between databases
National interoperability platform
koodistot.suomi.fi
Reference Data
BETK-BIM definitions
in use
under development
Message based
information sharing
(UN/CEFACT – XML)
N.N
a function or part of process
Legend
Call for tenders
Acceptance
Element product/ process data platform
ERP/
MRP
Centralised
architecture using
message based system
Master data ownership
Buildingsmart data dictionary (bsDD)
Building permit control
Status information
Despatch
Advice
Receipt Advice
Invoice
Despatch
Advice
Order
Response
Catalogue
221 Blanket Order
Order Response
Order Change
Order Response
CDE
Standardised design nomenclature
M-BOM
E-BOM
Element fabrication drawings
Purchase
Order
Delivery
ID:(S)GTIN/SSCC
    Data Carrier:128 barcode/DataMatrix/RFID
Receiving
Driving arrangement
226
Call off order
IFC
Element design
2D
designs
IFC
E-BOM
(if ETO parts)
Design
(if ETO parts)
M-BOM
Delivery information
(EPCIS)
eCMR
eFTI
Production
ID:SGTIN
Data carrier:
DataMatrix / RFID
Invoice
Delivery information
EPCIS
eCMR
eFTI
CDE
CDE
Peppol
network
Project shared data repository
(Common Data Environment)
Production
ID:(S)GTIN
Data carrier:
EAN / DataMatrix
FACILITY MANAGEMENT
Maintenance
Renovation
Demolition
CAFM
National product information database (TT/EMDG) and product identification (GS1/GTIN)
Data carriers
1D Barcode GS1 EAN / 128
2D Barcode GS1 DataMatrix
Passive UHF RFID
Information service or platform
DPP
EU Digital Product Passport
(JSON-LD)
?
?
Peppol
network
Peppol
network
MEP-BIM
STR-BIM
CAFM Computer Aided Facility Management
E-BOM Engineering Bill Of Materials
eCMR Electronic consignment note
eFTI Electronic freight transport information
EMDG European Master Data Guideline
EPCIS Electronic Product Code Information Services
ERP Enterprise Resource Planning
ETO Engineer-To-Order
GTIN Global Trade Item Number
M-BOM Manufacturing Bill Of Materials
MRP Material Resource Planning
MTS Make-To-Stock
SGTIN Serialized Global Trade Item Number
TT National product information standard
WMS Warehouse Management System
IFC
T005
Tender
Data platform/ERP/WMS
Data platform/ERP/WMS
EU:
Corporate Sustainability
Reporting Directive
IFC
Receipt
Advice
DPP
DPP
(MTS-parts)
Notes: This is our generated artefact ”distributed and open data architecture” figure.
Different colors represent a different phases and parties of the supply chain in bigger picture. At the top levels, we present public and private sector information services.
The white boxes illustrate functions or parts of the precast concrete element process.
The cylinders illustrate information services or platforms either in use or currently under development. For example, we are currently working on creating reference master data definitions on the Building Smart Data Dictionary platform.
Next, the ownership of master data by different stakeholders is shown.
5. Finally, the message-based system is highlighted, which facilitates the sharing of event data about process status, transportation details for deliveries, master data for products, and transactional data like invoices, orders, responses, catalogs, and notifications between stakeholders.
This chart is an evolving artefact, and we are continually refining it to make the architecture more precise and accurate to serve industry needs.

## Slide 25: Contents
Motivation
Background
  Manufacturing strategies
  T-Model
  Preliminary study on the current state of the ETO Supply Chain
Project Organization
Work Objective
  Road-map
  Future State Data Flow Architecture for an ETO products
Work Tasks
  Standardization work group
  API & IT infrastructure

## Slide 26: Work tasks
The BETK working group develops and standardizes solutions that support the flow of information and prepares application guidelines for the construction industry.
The BETK working group is divided into two subgroups that focus on data standardization and data transfer interfaces.
Collaboration Coordination Reporting
Application of GS1 standards
SC group: BETK
(Engineer-To-Order, ETO)
Standardization working group
Interface
working group
The main focus is on identifying and standardizing common industry practices.
Standardization of BIM modeling requirements
Process data definitions
Supply chain statuses
etc.
The main focus is on producing application guidelines for transferring supply chain-related data.
Peppol (transaction data)
EPCIS (event data)
eFTI (transport data)
EU DPP
etc.

## Slide 27: STANDARDIZATION working group
The task of the Standardization Working Group is to develop software-independent solutions that enable the automated generation and enrichment of standardized, machine-readable information at different stages of the supply chain.
Standardization of information enhances machine readability and facilitates the flow of information to the next stages of the supply chain.

## Slide 28
STANDARDIZATION working group
YHTEENTOIMIVUUSALUSTA
Koodistot-työkalu
The BETK working group defines the product and process information content for the precast concrete supply chain using interoperability platforms (buildingSmart Data Dictionary & koodistot.suomi.fi).
The purpose of this is to establish and maintain the semantic interoperability of information shared within the precast concrete supply chain, ensuring that the meaning of data remains consistent across information flows.
Instead of each organization independently defining the content of a concept and the related data, this description is created once on the interoperability platform. Other parties can then reference and apply this description.
Technically speaking, the vocabularies, code lists, and data model descriptions published on the interoperability platform are linked data, meaning they are uniquely identified web resources with permanent identifiers that can be referenced from elsewhere.
Notes: BETK-työryhmän tehtävänä on laatia vakioitu RAK-suunnittelukoodisto ja tietosisältömäärittely betonielementtitoimitusketjun osalta, joka julkaistaan koodistot.suomi.fi ja Building Smart Data Dictionary-sivustoilla.
Rakennetietomallien osalta BEC-tietokentät ovat vakiintuneet alan
epäviralliseksi standardiksi Suomessa, ja tietomallintamisen tilaaja
voi luottaa saavansa rakennetietomallit BEC-tietosisällöllä melko
luotettavasti kaikilta tietomallintavilta
rakennesuunnittelutoimistoilta. On kuitenkin huomattava, että
BEC-tietokenttien tietosisältöä ei ole varsinaisesti vakioitu, minkä
vuoksi muun muassa koneluettavuus on heikkoa. BEC toimii kuitenkin erinomaisena esimerkkinä,
kuinka vakiointi, vaikka vajavaisenakin, helpottaa yhteistyötä ja
kasvattaa toiminnan tehokkuutta.
Rakennusalalla nousseet uudet käyttötapaukset rakennuksen
elinkaaren aikana, erityisesti hankinta-valmistus-toimitus-asennus
-vaiheissa edellyttävät tietomalleilta tietosisältöjen vakiointia ja
uudenlaisia tietosisältöjä, mikä on todettu useaan kertaan mm.
Aalto yliopiston Building2030 tutkimushankkeessa,
Rakennusteollisuus Ry:n Betonielementti toimitusketju sekä
Talotekniikan toimitusketjun digitalisointi -projekteissa. Lisäksi
uuden Rakentamislain vaatimat tietomallimuotoiset suunnitelmat,
rakennusvalvonnan vaatimien tietomallien koneluettavuus ja
automaattinen tarkistaminen ja toteumamallien hyödyntäminen
edellyttävät tietomallien vakiointia.

## Slide 29: STANDARDIZATION working group
METATIETO
FI-Hankinta
Elementtityyppi
Raudoitus
Pintakäsittely
Hiertopinnat
Vähähiilinen
Status
Paino
Kerros
Lohko
The standardization of design data enhances the machine readability of product metadata and facilitates the flow of information to the next stages of the supply chain
Product: Nostolenkki S235J2+N PN32
GTIN:……………
Product: harvakierretanko
GTIN:……………
Product: P-työsaumaraudoite
GTIN:……………
TUOTETIETOKANTA
Did you know that the product database of Rakennustieto includes product information for casting accessories in a structural format compliant with the TT standard?
V-Väliseinä
VSP-Väliseinä (sei..
. . . . . . .

## Slide 30: INTERFACE working group
ERP
ERP
EPCIS
EPCIS
PEPPOL
PEPPOL
interface
interface
interface
interface
DB
DB
Manufacturer
Contractor
Site interface
The Interface Working Group is responsible for producing application guidelines for the implementation of open data transfer solutions for construction industry stakeholders. The group's goal is to create interface descriptions, taking cybersecurity into account, and outlining an exemplary architecture for the various parties in the supply chain.
DPP
The application of methods based on open data transfer standards promotes the flow of information.

## Slide 31
Standardised way to work
A non-standard way to work
Supplier
Information Exchange Solution
Receiver
Information
Notes: From an identification and data capture point of view, it is important to have a standard way of working, to have interoperability, regardless of who is sending and who is receiving the information.

## Slide 32
Utilizing Peppol messages in the order-to-delivery process of construction products?
More information:
www.valtiokonttori.fi/peppol
www.valtiokonttori.fi/peppol-info
https://bis.beast.se/
Peppol = a network, not a system
Optimizing the supply chain, not a single point.
Based on an international standard: ISO/IEC 19845: 2015
Used in the construction industry in other Nordic countries.
The State Treasury is the Peppol authority in Finland.
To connect to the Peppol network, a Peppol service provider and a compatible system (e.g., order management system, ERP system, etc.) are always required.
INTERFACE working group
Sender
Receiver
Operator
(Access point)
Operator
(Access point)
Peppol network
By adopting electronic procurement messages, information exchange shifts to system-to-system communication, streamlining the entire process—similar to how e-invoicing works.
Principle: No bilateral agreements, but a networked implementation that is as universally applicable as possible. Connect once, reach all.
ERP
ERP
API
API
API
API
Notes: Iso osa toimitusketjun tiedonvaihdosta käydään vieläkin sähköpostitse tai puhelimitse aiheuttaen tehottomuutta (sposteja hukkuu, tietoja näppäillään uudelleen, enemmän virheitä, ei automatiikkaa). Myös tärkeiden toimitusketjussa jaettavien tietojen, kuten tuotetietojen ja tilausten saapumisaikojen, kerääminen, analysoiminen ja esittäminen on epäjohdonmukaista ja raskasta, ellei jopa mahdotonta, koska informaatiota ei välitetä rakenteellisessa, helposti käsiteltävässä muodossa. Peppol on kansainvälinen verkosto, jonka kautta voi välittää esimerkiksi Peppolin mukaisia katalogeja, tilauksia, tilausvahvistuksia, laskuja ja logistiikan dokumentteja. Periaatteena: ei kahdenvälisiä sovituksia vaan mahdollisimman yleiskäyttöinen, verkostomainen toteutus. Liity kerran tavoita kaikki. Peppolissa ei tarvitse ottaa käyttöön kaikkea, voi ottaa käyttöön vain sen mitä tarvitsee. Loppukäyttäjä (organisaatio) liittyy Peppol-verkostoon sertifioidun Peppol-palveluntarjoajien välityksellä. Suomessa Peppolin rinnalla toimii kansallinen verkkolaskuverkko, jota verkkolaskupalveluntarjoajat / verkkolaskuoperaattorit ylläpitävät. Moni suomalainen verkkolaskuoperaattori on myös sertifioitu Peppol-palveluntarjoaja.

## Slide 33: Message based information sharing using Peppol-network
. . . .
Processing of order confirmations
Processing of delivery data
Delivery
Dispatch notification
Order confirmation
Order
CONTRACTOR
MANU-FACTURER
Call for tenders
Tender/product catalogue
Reception
Invoice
Invoicing and payment
Sales order
Delivery arrangement
Tender processing
Order change
Tracking of deliveries
EPCIS
Call off
Delivery time confirmation / Delivery note
Tracking of deliveries
FM
eFTI, eCMR
Tentative delivery schedule
Processing delivery confirmations
Delivery-Confirmation
Reception message & Complaint
Complaint handling
Storage & Installation
Element design & manufacture
Order Response
Call for Tenders T004
Tender T005
Order Change
Order Response
226 Call off order
Despatch Advice
Delivery information
invoice
Receipt Advice
Sender
Receiver
Operator
Operator
Peppol network
PART SUPPLIER
Tender/product catalogue
Catalog
Sales order
Order
Order Response
Development project is currently focusing to define transactional information shared through supply chain
221 Blanket Order
Order Response
Peppol
network
Peppol
network
Notes: In this future state data flow architecture diagram, transactional data exchange via Peppol messages has been considered across a wide spectrum between general contractor and manufacturer, as well as manufacturer and part supplier process steps. In a later presentation, Tom Partanen will explain how we have progressed so far in this national development project.

## Slide 34: INTERFACE working group
GTIN | 0640000000007
MTO | 000001
SERIAL | 000000000000001
CATEGORY | PRECAST CONCRETE
SUB-CATEGORY | INTERIORWALL
MANUFACTURER | BETK
COUNTRY OF ORIGIN | FINLAND
DIGITAL PRODUCT PASSPORT
INFORMATION
GS1 Digital link
DPP
Digital Product Passports (DPP) are set to revolutionize the construction industry by providing a standardized way to manage, enrich, and share information about construction products throughout the supply chain with producers, businesses, authorities, and consumers.
The BETK working group supports upcoming EU legislation by producing application guidelines for the digital, open, and interoperable management of the precast concrete supply chain.

## Slide 35
NEW! Conference article about future state (ETO) construction production model data flow architecture
CIB-W78-2024-paper_118
NEW! Implementation guideline UPID & AIDC for ETO products
https://betoni.com/rakentaminen/betk/betk-tulokset/
Available at:
BETK results and other ongoing activities
Notes: We have relaesed some results from our development project to our website. We have made a implementation guideline for engineer to order products, Conference article about future state construction production model data flow architecture. The Future state data flow architecture is also available.

## Slide 36: BETK results and other ongoing activities
LEVELS OF PRUDUCT IDENTIFICATIONS |  |  | 
Level 1: Product identification |  | GTIN | 
Level 2: Product variation identification |  | GTIN + MTO Variation number | 
Level 3 Individual product identification |  | GTIN + MTO Variation number + Serial number (SGTIN) | 
GS1 APPLICATION IDENTIFIERS (AI) TO IDENTIFY ENGINEER-TO-ORDER PRODUCTS (PRECAST CONCRETE ELEMENTS) |  |  | 
Minimum information requirements for the identification |  |  | 
(01) GTIN |  | 06400001000247 Example | 
(242) Made-To-Order (MTO) variation number |  | 123456 Example | 
(21) Serial number |  | 12345678910 Example | 
*Optional additional information for precast concrete elements |  |  | 
(91) Finnish element classification |  | V1001 Example | 
(92) GUID |  | ba34cf17-0c4b-4c6f-9295-cae05aa74ad4 Example | 
(99) Domain name |  | id.rt.fi Example | 
DATA CARRIERS |  |  | 
GS1 Digital Link (2D Barcode) | GS1 DataMatrix (2D Barcode) |  | EPC/RFID (radio frequency remote sensing method)
Identification and data-capture
36
Share
Product data Meta data
Event data GS1 EPCIS
Who: (GLN) Party
What: (SGTIN) Element
Where: (GLN) Factory
When: YYYY-MMDDThh:mm:ssZ
Why: Manufacturing
Status: Active
Transactional data Peppol-network

## Slide 37
GTIN 1
GTIN 2
GTIN 3
GTIN 4
GTIN 5
GTIN 6
EXAMPLE: use case of GS1 Product identification levels
Notes: To understand the logic behind of a GS1 three level hierachy levels, I’m showing one example.
Manufacturer could give GS1 GTIN codes to its basic products.

## Slide 38
GTIN 3
+ variation number 1
+ serial 1
GTIN 3
+ variation number 1
+ serial 2
GTIN 3
+ variation number 1
+ serial 3
GTIN 3
+ variation number 2
+ serial 1
GTIN 3
+ variation number 2
+ serial 2
GTIN 3
+ variation number 2
+ serial 3
GTIN 3
+ variation number 3
+ serial 1
GTIN 3
+ variation number 3
+ serial 2
GTIN 3
+ variation number 3
+ serial 3
GTIN 3 +
variation number 1
GTIN 3 +
variation number 2
GTIN 3 +
variation number 3
Notes: Product variants could have their own MTO variant numbers and each individual element could have its own serial number.

## Slide 39
The benefits of RFID are based on automated reading transactions ...and the resulting event data!
A read event means that the reader detects a specific RFID tag
Event data refers to the information related to this observation, linking it to business processes e.g. product, location, process step...
Notes: One of the data capture technologies we have defined as a suitable data carrier for eto products is passive ultra high frequency RFID technology, which has the benefits of automated reading transactions to support event data sharing.

## Slide 40
Passive UHF RFID-tags embedded in precast concrete
Placing RFID-tags to element
RFID-tunnisteisiin lisättiin etukäteen elementtien yksilöinti tiedot
Encoding UPID to passive UHF RFID tag
Elementtien toimitusvaiheessa RFID-tunnisteet luettiin käsilukijalla toisen kerran
Työmaalla, elementtien vastaanottovaiheessa RFID-tunnisteet luettiin automaattisesti kiinteällä lukijalla
Työmaalla, elementtien asennusvaiheessa RFID-tunnisteet luettiin käsilukijalla
Kuka: (GLN) Elementtitoimittaja
Mitä: (SSCC) Kuorma
Mitä: (SGTIN1, ..2, ..3) Betonielementit
Missä: (GLN) Tehdas
Milloin: YYYY-MM-DDThh:mm:ssZ
Miksi: Kuormaus
Status: Kuljetuksessa
What: (SGTIN) Precast concrete element
When: YYYY-MM-DDThh:mm:ssZ
Where: (GLN) Factory
Why: Active
Kuka: (GLN) Pääurakoitsija
Mitä: (SGTIN) Betonielementti
Missä: (GLN) Työmaa + tarkenne (huoneistossa tms.)
Milloin: YYYY-MM-DDThh:mm:ssZ
Miksi: Asentaminen
Status: Asennettu
Kuka: (GLN) Pääurakoitsija
Mitä: (SSCC) Kuorma
Mitä: (SGTIN1, ..2, ..3) Betonielementit
Missä: (GLN) Työmaa
Milloin: YYYY-MM-DDThh:mm:ssZ
Miksi: Vastaanotto
Status: Vastaanotettu
Kuka: (GLN) Rakennuksen omistaja
Mitä: (SGTIN) Betonielementti
Missä: (GLN) Rakennus + tarkenne (huoneistossa tms.)
Milloin: YYYY-MM-DDThh:mm:ssZ
Miksi: Elinkaarentapahtuma X
Status: Tapahtuma X
Design RFID-tag places to element
GS1 EPCIS
EXAMPLE: use case of AIDC technology for event data sharing
Notes: As part of our development project, we have been testing passive UHF RFID tags embedded in precast concrete.
Here is a visual demonstration of a process step for sharing event data from precast elements, which is one of our interests related to this development project that we have been testing.

## Slide 41: Yksilöinnin ja tunnistamisen pilotointi
Passiivisia UHF RFID-tunnisteita asennettiin 20 elementtiin
(3-4 tunnistetta per elementti)
RFID-tunnisteisiin lisättiin etukäteen elementtien yksilöinti tiedot
Elementtien valmistuksen jälkeen RFID-tunnisteet luettiin käsilukijalla
RFID tag reading during storage and loading on factory
Reading RFID tags when receiving and storing on site
Reading RFID tags when installing and inspecting on site
Kuka: (GLN) Elementtitoimittaja
Mitä: (SGTIN) Betonielementti
Missä: (GLN) Tehdas
Milloin: YYYY-MM-DDThh:mm:ssZ
Miksi: Valmistus
Status: Aktiivinen
Reading RFID tags during product life cycle activities
What: (SGTIN) Precast concrete element
When: YYYY-MM-DDThh:mm:ssZ
Where: (GLN) Factory
Why: loading
GS1 EPCIS
What: (SGTIN) Precast concrete element
When: YYYY-MM-DDThh:mm:ssZ
Where: (GLN) Site
Why: arriving
What: (SGTIN) Precast concrete element
When: YYYY-MM-DDThh:mm:ssZ
Where: (GLN) Site
Why: installed
What: (SGTIN) Precast concrete element
When: YYYY-MM-DDThh:mm:ssZ
Where: (GLN) Building
Why: other
GS1 EPCIS
GS1 EPCIS
GS1 EPCIS
Notes: EPCIS (Electronic Product Code Information Services) is a GS1 standard that enables the tracking and sharing of event-based supply chain data.
It records what happened, where, when, and why for individual products or shipments, allowing different stakeholders to exchange real-time, standardized information about the movement and status of goods.

## Slide 42
RFID-pilot

## Slide 44: More information about ongoing development project www.betoni.com/rakentaminen/BETK
Janne Kihula Teemu Alaluusua
Division Manager (precast concrete products) Project Manager, BETK
+358 40 514 6510 +358 40 826 8533
janne.kihula@rt.fi teemu.alaluusua@condigi.fi
Linkedin.com/in/teemu-alaluusua